THERMALLY IMPROVED (TIE) ALUMINUM WINDOWS - 08 51 13

With the thin lines that Milgard’s TIE Aluminum Windows provide, they are ideal for both new construction as well as replacement.  This series of products provide an economical solution while providing architectural style.

TIE Aluminum Windows

PART 1 – GENERAL

  - SUMMARY

- Section Includes:

      - Solid and tubular aluminum extruded windows of the following type(s):

Picture Window		Series 920, 921

Casement		Series 920, 921

Awning			Series 920, 921

Horizontal Slider	Series 1120

Vertical Slider		Series 1520

Bay Window		Series 1551

Bow Window		Series 1561

Radius			Series R20

B. 	Related Sections:

1.	 __ __ __ - _____________________.

2.	 __ __ __ - _____________________.

3.	08 32 13 – TIE Aluminum Sliding Doors.

C. 	Alternates:

1. 	Reference Section 01 23 00 – Alternates.

TIE Aluminum Windows  (continued)

  - SUBMITTALS

- Reference Section 01 33 00 – Submittal Procedures; submit following items:

  - Product Data.

  - Shop Drawings: Include window schedule, window elevations, sections and details, and multiple window assembly details.

  - Samples:

a. 	Color samples: Minimum 1x4 inch (25x100 mm) samples of Aluminum with painted or anodized color.

b. 	Glass, showing specified tint color.

4. 	Quality Assurance/Control Submittals:

a. 	Qualifications: Proof of manufacturer's qualifications.

b. 	U-Factor and structural rating charts required for AAMA and NFRC labeling requirements.

c. 	Installation Instructions – AAMA 2400 (“Mounting Flange Installation”)

- Closeout Submittals: Reference Section 01 78 00 – Closeout Submittals; submit following items:

  - Temporary window labels marked to identify windows that labels were applied to.

  - Maintenance instructions.

  - Special Warranties.

1.03      QUALITY ASSURANCE

- Overall Standards: Comply with ANSI/AAMA 101.I.S.2, except as otherwise noted herein.

- Qualifications:

1. 		Manufacturer Qualifications:

a. 	Minimum five years experience in producing aluminum windows of the type(s) specified.

  - Member AAMA, NFRC.

TIE Aluminum Windows (continued)

- Regulatory Requirements:

- Certifications for insulated glass windows:

#### AAMA: Windows shall be Gold Label certified with label attached to frame per AAMA requirements.

#### NFRC: Windows shall be NFRC certified with temporary U-factor label applied to glass and an NFRC tab added to permanent AAMA frame label.

1.04 	DELIVERY, STORAGE AND HANDLING

- Reference section 01 66 00 - Product Storage and Handling Requirements.

- Follow manufacturer’s instructions on label applied to windows.

1.05 	WARRANTY

- Residential Special Warranty:

#### Lifetime limited warranty to original owner.

#### Transferability:

  - Permit unlimited transfer of ownership in first ten years.

  - Upon first transfer of ownership, guarantee period shall become ten years from date of original purchase.

#### Warranty windows against defect in materials and workmanship including costs for parts and skilled labor.

- Commercial Special Warranty:

- 10-year warranty.

- Warranty windows against defects in manufacturing and workmanship including costs for parts and skilled labor.

TIE Aluminum Windows (continued)

PART 2 – PRODUCTS

2.01 	MANUFACTURER

- Milgard Manufacturing, Inc.	Tel:	1.800.MILGARD (645-4273)

1010 54th Avenue East		(253) 922-2030

Tacoma, WA 98424 	Fax:	(253) 926-0848

Web:	milgard.com

- Manufacturer’s Representative:

_________________________	Tel:	_______________

_________________________	Fax:	_______________

_________________________	Email:	_______________

- Window Series: Milgard TIE Aluminum Windows

- Substitutions: Reference Section 01 25 13 – Product Substitutions Procedures.

2.02 	MATERIALS

### Aluminum:  Comply with requirements of AAMA/WDMA/CSA 101/I.S.2/A440-05, 6063-T5 temper for strength, corrosion resistance and application of required finish.

### Extruded frame members are to be .060” in thickness for structural walls.

2.03	GENERAL PERFORMANCE REQUIREMENTS:

- Thermal Performance: Comply with NFRC 100.

- Air Leakage, Water Resistance, Structural Test: Comply with ANSI/AAMA 101/I.S.2.

- Forced-Entry Resistance: Comply with ASTM E 588.

TIE Aluminum Windows (continued)

2.04	WINDOW TYPES:

- Picture Window and Radius – [920 Series, 1-5/16” nail fin setback] [921 Series, block frame (no nail fin)] [R20 Series, 1-5/16” nail fin setback]:

1. 	Frame:

a.	920 Series, 2 ¼” (57mm)

b.	921 Series, 1 ½” (38mm)

c.	R20 Series, 2 ¼” (57mm)

2. 	Sightlines:

a.	920 Series, equal to 1 ¼”

b.	921 Series, equal to 1 13/16”

  - R20 Series, equal to 1 1/4”

3. 	Performance Class:

a. 	920 & 921 Series, 95 ½” x 71 ½” and smaller: F-HC45

b.	R20 Series, 71 ½” x 71 ½” and smaller: F-HC40

B.	Horizontal Slider – [1120 Series, 1 5/16” nail fin setback]:

1. 	Frame:

a.	1120 Series, 2 5/8” (67mm)

2. 	Sash: Depth of 1 1/8” (29 mm), solid aluminum extrusion.

3. 	Sightlines: Non-equal sightlines between sash and fixed glass.

4. 	Performance Class:

a. 	143 ½” x 59 ½” and smaller: HS-R20.

5.  	Hardware:

a. 	Nylon rollers with stainless steel axles, aluminum integral monorail track.

b. 	Single pull rail on meeting rail sash.

c. 	Automatic, spring loaded, height adjustable positive lock.

6.  	Weatherstripping: Fin seal polypropylene pile.

C.	Single Hung – [1520 Series, 1 5/16” nail fin setback]

1. 	Frame:

a.	1520 Series, 2 5/8” (67mm)

2. 	Sash: Depth of 1 1/8” (29 mm), solid aluminum profile.

3. 	Sightlines: Non-equal sightlines between sash and fixed glass.

4. 	Performance Class:

a. 	53 ½” x 89 ½” and smaller: H-LC25.

5. 	Hardware:

a. 	Concealed block and tackle balancer.

b. 	Single pull rail (sash lifts) on meeting rail sash.

c. 	Automatic, spring loaded, width adjustable positive lock.

6. 	Weatherstripping: Fin seal polypropylene pile.

D. 	Casement – [920 Series, 1 5/16” nail fin setback] [921 Series, block frame (no nail fin)]:

1. 	Frame:

a.	920 Series, 2 ¼” (57mm)

b.	921 Series, 1 ½” (38mm)

2. 	Sash: Depth of 1 1/2” (38mm), solid aluminum extrusion.

3. 	Performance Class:

a. 	95 ½” x 59 ½” Double Casement with center fixed, 36 vent set: C-C30.

4. 	Hardware:

a. 	Cam style locking mechanism with latch on jamb.

b. 	Tension adjustable hinge.

5. 	Weatherstripping: Dual durometer vinyl bulb seal.

E. 	Awning – [920 Series, 1 5/16” nail fin setback] [921 Series, block frame (no nail fin)]:

1. 	Frame:

a.	920 Series, 2 ¼” (57mm)

b.	921 Series, 1 ½” (38mm)

2. 	Sash: Depth of 1 1/2” (38mm), solid aluminum extrusion.

3. 	Performance Class:

a. 	48 ½” x 83 ½” Bottom Awning, 36” barset: AP-C30.

4. 	Hardware:

a. 	Cam style locking mechanism with latch on jamb.

b. 	Tension adjustable hinge.

5. 	Weatherstripping: Dual durometer vinyl bulb seal.

2.05	GLAZING

A. 	Insulated Glass Units: ASTM E 774, Class A, 1 inch (25 mm) thick overall except 1120/1520 series, which are 3/4 inch (19mm) thick.

1. 	Glazing Type: [Clear/Clear] [Clear/SunCoat® Low-E] [Clear/SunCoat® Low-E, argon gas filled] [Clear/SunCoatMAX™ Low-E] [Clear/SunCoatMAX™ Low-E, argon gas filled] [Clear/Hardcoat Low-E] [Clear/Hardcoat Low-E, argon gas filled].

2. 	Spacer Bar: [Warm edge steel spacer] [Aluminum box spacer] [Warm edge foam spacer].

2.06	DIVIDED LITE GRIDS

A. 	[5/8 inch (16 mm) wide flat, grids between the glass that are color matched to frame and sash] [1-1/16 inch (27 mm) wide sculptured, grids between the glass that are color matched to frame and sash]

2.07	INSECT SCREENS

A. 	Provide tight-fitting screen for operating sash with hardware to allow easy removal.

1. 	Screen Cloth: Charcoal colored fiberglass mesh.

2. 	Frame:

a. 	Cambered formed aluminum with rigid plastic corner keys.

b. 	Pull tabs for removal.

2.08	FABRICATION

A. 	Fabricate frames and sash with mechanically joined corners. Corners are fastened with corrosion resistant screws and sealed with an acrylic sealant.

C. 	All fixed glass is exterior glazed and all sashes are marine glazed with flexible PVC glazing.  The fixed glazing shall be removed without disassembly of a sash.  The vents will need to be disassembled to replace the glazing.

2.09	FINISHES

A.	Frame and Sash Color: [Bronze] [Clear] Anodized Exterior Finish:  Provide AA-C22-A32 Class II Bronze or AA-C22-A31 Class II Clear finish, minimum 0.4 mils thick, electrolytically deposited color anodized finish.

### B.	Color match screen frame to window frame and sash color.

2.10 	SOURCE QUALITY CONTROL

- Windows inspected in accordance with manufacturer’s Quality Control Program as required by AAMA Gold Label certification.

PART 3 - EXECUTION

3.01 	EXAMINATION

A. 	Examine openings in which windows will be installed.

1. 	Verify that framing complies with AAMA 2400 (“Mounting Flange Installation”) or AAMA 2410 (“Flush Fin Installation”).

2. 	Verify that fasteners in framed walls are fully driven and will not interfere with window installation.

B. 	Coordinate with responsible entity to correct unsatisfactory conditions.

C. 	Commencement of work by installer is acceptance of substrate conditions.

3.02 	INSTALLATION

- Install windows in framed walls in accordance with AAMA 2400 (“Mounting Flange Installation”) or AAMA 2410 (“Flush Fin Installation”).

- Do not remove temporary labels.

- Install insect screens on operable sash.

3.03 	CLEANING

- Reference Section 01 74 00 – Cleaning and Waste Management.

- Remove temporary labels and retain for Closeout Submittals.

- Clean soiled surfaces and glass using a mild detergent and warm water solution with soft, clean cloths.

END OF SECTION

This specification was prepared by Milgard Manufacturing, Inc. Comments or suggestions for improvement should be addressed to Milgard at the address in Article 2.01 A.

Issue Date: March 26, 2021

# Text boxes

3 Part Specification

Thermally Improved Aluminum | A250 Windows

SPECIFICATION BEGINS ON THE FOLLOWING PAGE.

GENERAL NOTES TO SPECIFIER:

THIS SPECIFICATION SYSTEM HAS BEEN PREPARED TO ASSIST DESIGN PROFESSIONALS IN THE PREPARATION OF PROJECT OR OFFICE MASTER SPECIFICATIONS. IT FOLLOWS GUIDELINES ESTABLISHED BY THE CONSTRUCTION SPECIFICATIONS INSTITUTE, AND THEREFORE MAY BE USED WITH MOST MASTER SPECIFICATION SYSTEMS WITH MINOR EDITING.

EDIT CAREFULLY TO SUIT PROJECT REQUIREMENTS. MODIFY AS NECESSARY AND DELETE ITEMS THAT ARE NOT APPLICABLE. VERIFY THAT REFERENCED SECTION NUMBERS AND TITLES ARE CORRECT (NUMBERS AND TITLES REFERENCED ARE BASED ON MASTERFORMAT, 2004 EDITION.)

THIS SECTION ASSUMES THE PROJECT MANUAL WILL CONTAIN COMPLETE DIVISION 1 DOCUMENTS INCLUDING 01 25 13 – PRODUCT SUBSTITUTION PROCEDURES, SECTIONS 01 33 00 – SUBMITTAL PROCEDURES, 01 62 00 – PRODUCT OPTIONS, 01 66 00 – PRODUCT STORAGE AND HANDLING REQUIREMENTS, 01 74 00 – CLEANING AND WASTE MANAGEMENT, 01 77 00 – CLOSEOUT PROCEDURES, AND 01 78 00 –CLOSEOUT SUBMITTALS. CLOSE COORDINATION WITH DIVISION 1 SECTIONS IS REQUIRED. IF THE PROJECT MANUAL DOES NOT CONTAIN THESE SECTIONS, ADDITIONAL INFORMATION SHOULD BE INCLUDED UNDER THE APPROPRIATE ARTICLES.

THIS IS AN OPEN PROPRIETARY SPECIFICATION ALLOWING USERS THE OPTION OF APPROVING OTHER MANUFACTURERS THAT COMPLY WITH THE CRITERIA SPECIFIED HEREIN.

NOTES TO THE SPECIFIER ARE CONTAINED IN BOXES AND SHOULD BE DELETED FROM FINAL COPY.

OPTIONAL ITEMS REQUIRING SELECTION BY THE SPECIFIER ARE ENCLOSED WITHIN BRACKETS, E.G. [35] [40] [45]. MAKE APPROPRIATE SELECTIONS AND DELETE OTHERS.

ITEMS REQUIRING ADDITIONAL INFORMATION ARE UNDERLINED BLANK SPACES, E.G. _______________________.

OPTIONAL PARAGRAPHS REQUIRING SELECTION OF ONE OF THE OPTIONS ARE SEPARATED BY “OR” WITHIN A BOX. E.G.

BOLD FACE TYPE IDENTIFIES OPTIONAL PARAGRAPHS AND FEATURES THAT MAY BE INCUDED OR DELETED DEPENDING UPON PROJECT REQUIREMENTS. CONVERT THE BOLD FACE TYPE TO REGULAR TYPE WHEN INCLUDING THESE PARAGRAPHS OR FEATURES.

REVISE FOOTER TO SUIT PROJECT/OFFICE REQUIREMENTS.

ELECTRONIC VERSIONS OF THIS SPECIFICATION UTILIZE AUTOMATIC PARAGRAPH NUMBERING.

WHEN EDITING IS COMPLETE, DELETE ALL TEXT ON THIS PAGE, THEN REMOVE THE SECTION BREAK AT THE TOP OF THE NEXT PAGE TO REMOVE THIS PAGE FROM THE DOCUMENT.

3 Part Specification

Thermally Improved Aluminum | A250 Windows

INSERT APPROPRIATE SECTION NUMBERS AND TITLES BELOW FOR WINDOW FLASHING AND INSTALLATION SEALANTS.

INCLUDE APPROPRIATE LANGUAGE BELOW IF PRODUCTS SPECIFIED IN THIS SECTION ARE TO BE BID AS ALTERNATES.

OTHERWISE DELETE FOLLOWING PARAGRAPH.

INSERT LOCAL REGULATORY REQUIREMENTS BELOW.

SELECT “RESIDENTIAL” WARRANTY BELOW FOR OWNER OCCUPIED SINGE FAMILY RESIDENTIAL AND OWNER OCCUPIED CONDIMINIUM PROJECTS.  SELECT “COMMERCIAL WARRANTY FOR NON-OWNER OCCUPIED CONDOMINIUMS, COMMERCIAL, AND MULTI-FAMILY PROJECTS.

OR

INSERT NAME, ADDRESS AND PHONE NUMBERS OF MANUFACTURER’S REPRESENTATIVE BELOW

VERIFY THAT WINDOW FLASHING MATERIAL AND INSTALLATION SEALANT IS SPECIFIED IN APPROPRIATE SECTIONS.

SELECT FOLLOWING WINDOW TYPES AND RELATED NAIL FIN/MOUNTING STYLE BASED ON PROJECT REQUIREMENTS. DELETE WINDOW TYPES NOT USED.

WARM EDGE SPACERS ARE NOT AVAILABLE ON SOME UNITS

INCLUDING CERTAIN OVERSIZE UNITS, RADIUS AND GABLED UNITS.

MOST COMMON TYPES OF INSULATED UNITS ARE INCLUDED ABOVE, BUT SEVERAL OTHER TYPES INCLUDING TINTED, REFLECTIVE, HEAT STRENGTHENED, TEMPERED, OBSCURE, WIRE, AND LAMINATED ARE AVAILABLE FOR SPECIAL APPLICATIONS. SELECT DESIRED TYPES FROM MILGARD WEBSITE milgard.com/architects AND SPECIFY IN LIEU OF, OR IN ADDITION, TO THE ABOVE WITH ALL NECESSARY CRITERIA SUCH AS OBSCURE PATTERNS. IF MORE THAN ONE TYPE OF GLAZING IS REQUIRED FOR THE PROJECT, BE CERTAIN THAT TYPE FOR EACH WINDOW IS CLEARLY NOTED ON DRAWINGS OR IN WINDOW SCHEDULE.

VERIFY THAT DESIRED GRID PATTERNS, IF ANY, ARE SHOWN ON THE DRAWING. CERTAIN GRID PATTERNS MAY NOT BE AVAILABLE WITH ONE OR THE OTHER BAR TYPES IN THE FOLLOWING PARAGRAPH - CONSULT MILGARD FOR UNUSUAL DESIGN APPLICATIONS. GRIDS ARE NOT AVAILABLE FOR SINGLE PANE GLASS WINDOWS.

INSTALLATION INSTRUCTIONS (AAMA 2400) ARE ADEQUATE FOR NORMAL INSTALLATION CONDITIONS IN FRAMED CONSTRUCTION. MASONRY WALLS AND UNUSUAL CONDITIONS MAY REQUIRE ADDITIONAL INFORMATION IN THIS ARTICLE.